## Slide 1: Science Olympiad Flying Events
Slides by Chuck Andraka and Jeff Anderson
NFFS Education Committee
Chuck Andraka

## Slide 2: Presentation Order
Event descriptions and rules
  Common areas
  Electric Wright Stuff B
  Wright Stuff C
Sources of materials and aid
Building techniques
Flying

## Slide 3: Common Rules B&C Division Events
Indoor Airplane Duration

## Slide 4: WS and EWS Event Description
Prebuild event
Powered Indoor Monoplane Airplane flown for Duration
Made with any materials except Boron
Best of two flights duration
Kits are permitted
Student-Built

## Slide 5: WS and EWS Event Direction
NOT a design event, but a flight optimization event
Data collection and recording is critical to success
BUILD LIGHT, try to reach the minimum allowed weight
Build accurately. Crooked, twisted planes do not fly well
Take LOTS of data == Fly A Lot

## Slide 6: Common Event Parameters
Kit, plans, or self-design
  No pre-glued or pre-covered
45cm wing span, 9cm chord
28 cm stab span, 7cm chord
Do not push the dimensions. Too big and you will be tiered
Propeller built or purchased
10% bonus for BLACK MARKER between 2 ribs or one tip plate
Labelled for identification
Up to 2 planes presented for inspection
2-Student team
Non-compliant planes tiered

## Slide 7: Common Event Parameters NOT MENTIONED
Plane configuration
  Canard vs. Conventional
  Tractor vs. pusher
Length of plane
Format of wing (flat with tip plates, dihedral)

## Slide 8: Common Event Flying Process
Indoors, with room dimensions published in advance
No coaching or communication once in event
ONLY PARTICIPANTS may touch plane. This means DO NOT let officials attempt to measure
Flight log: 30% penalty if not presented, 10% if incomplete
Trim flights permitted, but on the clock, and must be announced as trim
Clock
  8 minute period starting with first flight, trim or official, or end of preflight time period
  Trim flight may be unpowered
  Prep period before 8-minute window, starts when rubber or charger handed to student. 5% bonus if start a flight in prep window. 3 minutes WS, 2 minutes EWS
  No time-out for retrieval or repairs
  A flight starting in 8 minute window may go to completion
Score best duration of 2 official flights, plus bonuses
Construction violations are tiered

## Slide 9: Common Event Flight Log
Logs are critical to learning, trimming, improving
Missing log is 30% penalty
Incomplete log is 10% penalty
Required and student selected entries
10 flights minimum
Numeric values must be in proper metric units
AAHS ELG Log 2018-2019 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Date | Flight | Plane | CG behind LE (mm) | TE Shim Height(mm) | Left Flap Stiffness (g) | Right Flap Stiffness (g) | Rubber length (cm) | Rubber width (g/in) | Rubber stretch Length (in) | Angle Launch (deg) | Tilt Launch (deg) | Duration (sec) | Altitude (ft) | Notes

## Slide 10: Common Event Build Log
New Requirement as part of flight log
Must include:
  Materials used in construction of plane
  Labeled diagram identifying and describing parts of the plane
  Appropriate metric units for all numeric values
  Cover page with team name and number
If CNC machines (3-D printer, CNC router, laser cutter) are used to build the device or any component thereof, additional log requirements
  Information about the tool, software, and materials used
  Details of any source digital files (CAD, STL, OBJ, etc.) including where it was obtained, web link if downloaded
  Description of how the final device was constructed from the tool-created components
Students must be able to answer questions regarding the design, construction, and operation of the plane

## Slide 11: ES Experience Issues and Observations
Insufficient Logs
  Only 10 entries (or less)
  Too few columns
  Logs are a critical element of improvement
Crooked construction
  Accurate construction is critical
Untrimmed models
Heavy models: Too much glue!
Most planes reasonably built, but not reasonably trimmed
  Need to do a circle for any reasonable duration
  Trim plane for low power, then work on higher power adjustments
Not flying the same in practice and competition
  Do not let observations of others change your approach!

## Slide 12: Thoughts for improvement
This year’s plane should be a joy to fly: Good proportions, stable platform
Spend more time in gym than in build
Keep detailed logs
Read and follow rules carefully
Very good online videos on trimming at J&H
Use resources, especially the online forum at Scioly

## Slide 13: Electric Wright Stuff B
Indoor Capacitor Powered Duration

## Slide 14: Electric Wright Stuff Additional Event Parameters
Powered by a 5F, 3V Super Capacitor
Charged up to 3.0V from 2 alkaline cells up to D size
Direct Drive Prop
  Prop size not specified
  No gearbox
9.5g minimum mass
Battery and capacitor labels (ratings) must be viewed by judges
On-plane power system may consist of propeller, motor, capacitor, switch, wires, connectors
Charger may consist of batteries, battery holder, wiring, connectors, and a resistor
Note: Wires weigh a LOT. Experiment with finer wires to save weight without losing voltage

## Slide 15: Electric Wright Stuff Event Flight Log
Required entries
  Charging duration (seconds) or capacitor voltage at launch
  Flight Time
  Estimated or measured altitude
At least three additional column
  Charge remaining at landing
  Decalage measurements
  Center of gravity
  Any other
10 flights minimum

## Slide 16: Thoughts for EWS
Electrical components may be in short supply, so order early
Electrical components can be purchased at typical electrical suppliers such as Digi-Key, Newark, Mouser, Arrow, or at Amazon
Motors are not all created equal
  Probably 6mm to 8mm motor size
  Be sure to check kV rating (thousands of RPM per volt) or RPM at 3 volts!
    Some drone motors will turn 40,000 or more. Way too high!
    “Pager” motors are around 10-12,000 RPM at 3v, more suitable
Many props are available
  Drones
  Airplanes
  Probably want something around 35-60mm diameter
  Check prop shaft hole size against motor shaft size

## Slide 17: Wright Stuff C
Indoor Rubber Powered Duration

## Slide 18: Wright Stuff Additional Event Parameters
24cm diameter prop maximum
Propeller built or purchased
8g minimum without rubber
  9.5g flying weight
Rubber powered
  1.5g maximum rubber mass
  Includes any o-rings
  Before or after lube
  6 rubber motors may be processed

## Slide 19: Wright Stuff Event Flight Log
Required entries
  Motor size (length, width, mass)
  Number turns or torque AT LAUNCH
  Flight Time
Three additional minimum column
  Altitude
  Torque
  Remaining turns or torque
  Unwinds
  Propeller details
  Any other
Log is critical to improving
AAHS Wright Stuff Log 2018-2019 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Date | Flight | Plane | Propeller | Prop Pitch | Prop Flex (g) | CG behind TE (mm) | LE Height (mm) | TE Height (mm) | Stab LE height (mm) | Stab TE height (mm) | Rubber length (cm) | Rubber width (g/in) | Rubber mass (g) | Number Winds | Number unwind | Net Winds Launch | Torque Max | Torque at Launch | Duration (sec) | Altitude (ft) | Turns Remianing | First lap altitude | Notes

## Slide 20: Sources
Kits
Supplies
Help

## Slide 21: Kits
Ward’s Science
  Official Science Olympiad Supplier
  “Kit” includes tools, glues, etc. to get you started
  Generally more “Open Ended” than other kits
    Less direct design and guidance
    Not as refined

## Slide 22: Kits
Freedom Flight Models
  Complex but competitive, consistently in top 10 at Nationals
  Consistent quality
  EXTENSIVE instructions
  https://www.freedomflightmodels.com
Also a full stock of accessories
  Torque meter
  Winder
  Counter
  Rubber
  Propellers

## Slide 23: Kits
J&H Aerospace
  Competitive indoor flyer designs
  Many good YouTube videos
  https://jhaerospace.com/

## Slide 24: Kits
Laser Cut Planes
  Simple building
  Operable design
  Low cost
  Photo-instructions, no plans
  https://lasercutplanes.com/
  Known for simple assembly

## Slide 25: Kits
Guru Engineering
  Recent addition
  Based out of WV, supported WS win at Nationals 5 years ago
  Non-profit
  Lowest cost options
  http://main.guruengineeringtech.com/

## Slide 26: Accessories
Rubber, Props, Winders, Torque meters, covering
  Indoor Free Flight Supply
    https://www.indoorffsupply.com/
  Freedom Flight Models
    https://www.freedomflightmodels.com
  FAI Model Supply
    https://www.faimodelsupply.com/
  J&H Aerospace
    https://jhaerospace.com/
Covering, prop hangers, rubber stripper
  Indoor Model Specialties
    http://www.indoorspecialties.com/

## Slide 27: Resources and help
Plans
  Hip Pocket Aeronautics
    http://www.hippocketaeronautics.com
    Look for Bill Gowen and Brian Turnbull
Online Resources
  National Free Flight Society at https://freeflight.org/join-learn-fly/science-olympiad/ includes videos, plans, how-to guides, etc.
  SCIOLY online forums at https://scioly.org/forums/viewforum.php?f=283
  Hip Pocket Aeronautics forums https://www.hippocketaeronautics.com/hpa_forum/index.php?board=33.0
  Minimizing weight gain: https://www.soinc.org/sites/default/files/uploaded_files/glueweight.pdf
  Basic Building: https://www.soinc.org/sites/default/files/uploaded_files/ScienceOlympiad5.0.pdf

## Slide 28: Building Techniques

## Slide 29: Building
Weight is EVERYTHING
  Glue control
    Thin CyA
    Capillary applicator
  Balsa Density
    Weigh and grade balsa
    Bring scale to store
    5-8 lb/cu ft best
    Kits have excellent wood
Straight
  Use fixtures
    Foam board allows pins
  Glass or shelving surface
Strength
  Wrap key joints with thread, dot of CA
  Carbon is light, stiff

## Slide 30: Covering
Ultrafilm is used in most kits
  Grocery veggie bags a decent backup
Prepare
  Build structure
  Build a frame scrap balsa
Film
  Cut with solder iron if available, tears easily
  Ball up as small as possible, twice
  Unfurl with outward stretching motion
  Attach to frame with lip balm or Vaseline
  Carefully stretch to edges, not tight
Adhesive
  3M 77 is best (easy, light enough)
    Glue stick an alternative
  Light coating on top of structure separate from covering
  Press into framed film inverted
  Allow to cure
  Cut with soldering iron
    Careful not to dwell on carbon

## Slide 31: Flying Techniques

## Slide 32: Trimming
Verify mass
  Check often, remove ballast as glue is added
  Use modeling clay
Verify CG often
Decalage to about 3-8mm
Wind lightly, 600 turns (60 on 10:1)
Launch straight ahead with light toss
Watch for stall
  Increase wing incidence until stall observed
  Decrease until stall just goes away
Watch for recovery from touches (ceiling)
  If dives, move CG forward and re-trim
  If quick recovery, may try more aft CG
Trimming may take one or more flying sessions

## Slide 33: Trimming (cont.)
Higher power launches
Adjust launch torque to room height
If roll in, add inboard wing wash-in (raise leading edge of left, or inner wing)
Rudder has greater effect on high speed
Tail tilt has greater effect on low speed

## Slide 34: Wright Stuff Flying
Record ALL parameters in log
  Change ONE THING at a time
Rubber/prop optimization is key
  Change props
  Adjust prop (pitch, flex)
  Rubber width, length
  Stopwatch tells the tale
  If it won’t climb, try thicker rubber, less pitch, or less diameter
Half rubber flights
  ½ altitude, ½ time
  ½ rubber length, same thickness
  Predictable higher ceiling performance
  Lower risk
  Replace ½ rubber with weighted stick
GET IN THE GYM
  Winning takes many flights

## Slide 35: Wright Stuff Flying
Rubber winding
  Hysteresis
  Wind off airplane!
  Torque meter
  Wind counting
  Lubricate
    Silicon oil
    Armorall
  Wind to almost breaking (break some to know)
    Usually based on torque
  Back off to launch torque
    Ceiling height
Stretch winding
  Stretch to 7-8X length
  Wind ½ at full stretch, then walk in
Rubber evaluation
  Initial climb: Launch torque
  Cruise: rubber/prop balance
  Letdown: Prop flex
  Look at turns remaining
    Ideally about ½ row of knots

## Slide 36: Electric Wright Stuff Flying
Record ALL parameters in log
  Change ONE THING at a time
Start with low power
  Charge less, to a lower voltage
  Run-off charge before launching
Increase voltage to gain more altitude
Adjustments
  Prop pitch: Heat and twist or just twist
    Need a pitch gage for accuracy
    More pitch means more climb, shorter duration
  Prop diameter: Don’t be afraid to cut down a prop that climbs too much
  CG and decalage may help control altitude
Estimating altitude using basketball hoop (10 feet)
GET IN THE GYM
  Winning takes many flights

## Slide 37: Flight Adjustments
If initial flights are decent, make SMALL changes and record differences
Dives:
  Increase decalage: Raise front of wing or back of tail stabilizer
  Move CG rearward
Stalls (nose climbs then dips repeatedly)
  Decrease decalage
  Move CG forward
Stalls only at high power
  Add down thrust (angle propellor shaft downward)
  Add incidence to BOTH surfaces (raise leading edge of wing AND stab)
Flight is ok but climb limited
  EWS increase pitch, WS decrease pitch
  Add left wing wash-in (raise left wing leading edge slightly)
  Increase decalage until stall, then back off slightly

## Slide 38: Follow-up
Chuck Andraka
ceandra@comcast.net
(505)974-0380 (text preferred)
CoachChuckAAHS on Scioly Forum